## Slide 1: A Mobile Traffic Predictor Enhanced by Neighboring Transportation Data (MTP-NT)
Patrick Luiz de Araújo
Programa de Pós-Graduação em Ciência da Computação
Defesa de dissertação de mestrado em ??/??/????

## Slide 2: Contents
Introduction
Related Work
Preliminaries on data collection for MTP-NT
Framework structure and fundamentation
Experimental results
Final considerations and future work

## Slide 3: Data per month, per smartphone in 2028
19 GB/month
5G subscribers in 2028
5 billion
Data per quarter in 2028
100 exabytes
Introduction
Fonte: Ericsson Mobility Report, November 2022

## Slide 4
To
Allocate the maximum amount of users
Introduction
New 5G networks will count on
Core Network (CN) based on Virtual Network Functions (VNF) over a Network Function Virtualization (NFV)2 topology
Cloud and edge computing3
Use Machine Learning (ML) and other predictive tools
Optimize network operability
Reach 5G QoS/QoE metrics1
1ms latency
low energy consumption
High coverage
[1] AGIWAL, M.; ROY, A.; SAXENA, N. Next generation 5g wireless networks: A comprehensive survey. IEEE Communications Surveys Tutorials, v. 18, n. 3, p. 1617–1655, 2016.
[2] Sun, Y. et al. Application of machine learning in wireless networks: Key techniques and open issues. IEEE Communications Surveys Tutorials, v. 21, n. 4, p. 3072–3108, 2019.
[3] ALAWE, I. et al. Improving traffic forecasting for 5g core network scalability: A machine learning approach. IEEE Network, v. 32, n. 6, p. 42–49, 2018.
Intelligent caching in network edge
Cloud computing optimization
Notes: NFV: topologia usando cloud e/ou edge
Estruturas com a capacidade que necessitam, economizando recursos
Vai passar a ter gerenciamento de rede unificado

## Slide 5
AI models advantages
Introduction
Limitants
Enough data?
Pertinent information?
Response time
Return Over Investiment – ROI
Rely on historical data123
Can be less complex than conventional approaches4
Robust patterns and best overall performance5
[1] Wang, X. et al. Spatio-temporal analysis and prediction of cellular traffic in metropolis. In: 2017 IEEE 25th International Conference on Network Protocols (ICNP). [S.l.: s.n.], 2017. p. 1–10
[2] Wang, J. et al. Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. In: IEEE INFOCOM 2017 - IEEE Conference on Computer Communications. [S.l.: s.n.], 2017. p. 1–9.
[3] CHEN, X. et al. Analyzing and modeling spatio-temporal dependence of cellular traffic at city scale. In: 2015 IEEE International Conference on Communications (ICC). [S.l.: s.n.], 2015. p. 3585–3591.
[4] SUN, H. et al. Learning to optimize: Training deep neural networks for wireless resource management. In: 2017 IEEE 18th International Workshop on Signal Processing Advances in Wireless Communications (SPAWC). [S.l.: s.n.], 2017. p. 1–6.
[5] Sun, Y. et al. Application of machine learning in wireless networks: Key techniques and open issues. IEEE Communications Surveys Tutorials, v. 21, n. 4, p. 3072–3108, 2019.
Notes: Modelos de IA
Dependem de dados históricos
Menos complexos: implementação de um alocador de potência menos complexo que o Weighted Minimum Mean-Square Error (WMMSE)

## Slide 6
Opportunities
Introduction
Limitants
Enough data?
Pertinent information?
Response time
Return Over Investiment – ROI
Rely on historical data123
Can be less complex than conventional approaches4
Robust patterns and best overall performance5
[1] Wang, X. et al. Spatio-temporal analysis and prediction of cellular traffic in metropolis. In: 2017 IEEE 25th International Conference on Network Protocols (ICNP). [S.l.: s.n.], 2017. p. 1–10
[2] Wang, J. et al. Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. In: IEEE INFOCOM 2017 - IEEE Conference on Computer Communications. [S.l.: s.n.], 2017. p. 1–9.
[3] CHEN, X. et al. Analyzing and modeling spatio-temporal dependence of cellular traffic at city scale. In: 2015 IEEE International Conference on Communications (ICC). [S.l.: s.n.], 2015. p. 3585–3591.
[4] SUN, H. et al. Learning to optimize: Training deep neural networks for wireless resource management. In: 2017 IEEE 18th International Workshop on Signal Processing Advances in Wireless Communications (SPAWC). [S.l.: s.n.], 2017. p. 1–6.
[5] Sun, Y. et al. Application of machine learning in wireless networks: Key techniques and open issues. IEEE Communications Surveys Tutorials, v. 21, n. 4, p. 3072–3108, 2019.
Notes: Modelos de IA
Dependem de dados históricos
Menos complexos: implementação de um alocador de potência menos complexo que o Weighted Minimum Mean-Square Error (WMMSE)

## Slide 7: tl;dr
Enough Data
Innovation
Compatible responsiveness
Performance
Notes: Estes são os desafios a atentar-se em uma implementação de ML em 5G

## Slide 8: Mobile Traffic Predictor Enhanced by Neighboring Transportation Data MTP-NT
City of Milan Dataset1
Scalable public transport and neighboring data
Open source
Lightweight, adaptable and highly performant
State-of-art performance
Network usage
Geolocalized tweets
Weather
Electricity
News
[1] Barlacchi, G. et al. A multi-source dataset of urban life in the city of milan and the province of trentino. Sci Data 2, 2015.
Notes: Dados
GDPR: politica de dados robusta
Dados de 1/nov/2013 até 31/dez/2013
Inovação
Uso pioneiro de dados de transporte público
Dados e modelagem abertas
Leve
Escalável através do volume de dados ingeridos
Vários volumes validados
Performático
Performance
Mas também oportunidade
80% das torres carregam 20% do tráfego;
50% carregam 5%;
0,35% carregam 50% de todo o volume

## Slide 9: Contents
Introduction
Related Work
Preliminaries on data collection for MTP-NT
Framework structure and fundamentation
Experimental results
Final considerations and future work

## Slide 10: Metrics and mathematical characteristics of network usage
Related work
Characterization
Prediction
Mathematical models to predict network traffic

## Slide 11: Regions of the city grouped based on network usage patterns1 Composition of trimodal distributions to describe the network traffic2 Sand temporal distribution of the network traffic results into extremely insufficient utilization of network resources2 Traffic was concentrated in some regions (city center) and peak hours3
Related work - Characterization
[1] Xu, F. et al. Understanding mobile traffic patterns of large scale cellular towers in urban environment. IEEE/ACM Transactions on Networking, v. 25, n. 2, p. 1147–1161, 2017.
[2] WANG, H. et al. Characterizing the spatio-temporal inhomogeneity of mobile traffic in large-scale cellular data networks. In: Proceedings of the 7th International Workshop on Hot Topics in Planet-Scale MObile Computing and
Online Social NeTworking. New York, NY, USA: Association for Computing
Machinery, 2015. (HOTPOST ’15), p. 19–24. ISBN 9781450335171. Disponível em: <https://doi.org/10.1145/2757513.2757518>.
[3] Gotzner, U.; Rathgeber, R. Spatial traffic distribution in cellular networks. In: VTC
’98. 48th IEEE Vehicular Technology Conference. Pathway to Global Wireless
Revolution (Cat. No.98CH36151). [S.l.: s.n.], 1998. v. 3, p. 1994–1998 vol.3.
Notes: Em (1)
Regiões da cidade são agrupadas com base no seu padrão de uso
Padrão de uso evidenciam a natureza organizacional da cidade
Indicando correlação e causualidade

## Slide 12
[1] BOUTABA, R. et al. A comprehensive survey on machine learning for networking: evolution, applications and research opportunities. Journal of Internet Services and Applications, Springer, v. 9, n. 1, p. 1–99, 2018.
[2] CYBENKO, G. Approximation by superpositions of a sigmoidal function. Mathematics of control, signals and systems, Springer, v. 2, n. 4, p. 303–314, 1989.[3] Funahashi, 1989
[4] HORNIK, K. Approximation capabilities of multilayer feedforward networks. Neural networks, Elsevier, v. 4, n. 2, p. 251–257, 1991.[5] Wang, 2017a
[6] Wang, X. et al. Spatio-temporal analysis and prediction of cellular traffic in metropolis. In: 2017 IEEE 25th International Conference on Network Protocols (ICNP). [S.l.: s.n.], 2017. p. 1–10.
[7] YANG, H. et al. A network traffic forecasting method based on sa optimized arima–bp neural network. Computer Networks, v. 193, p. 108102, 2021. ISSN 1389-1286. Disponível em: <https://www.sciencedirect.com/science/article/pii/ S1389128621001821>.
Related work - Prediction
Pure Time Series Function (TSF) and Non-TSF problem1
Multi Layer Perceptrion (MLP) to traffic perdiction2
Single Layer Perceptron (SLP) to traffic perdiction3
MLP to network traffic forecasting4
Recurrent Neural Network and usage of global + local autoencoders5
In-tower and inter-tower traffic analysis through a Graph Neural Network (GNN)6
AutoRegressive Moving Average (ARIMA) and Neural Network model training with Simulated Annealing (SA)7
2021
2017
1991
1989

## Slide 13: 2844 Base Stations (BSs) in Suzhou 500m2x 500m2 Uses the neighborhood concept LSTM Cells paired with Global and Local Autoencoders
Related work – Wang 2017a
Source: Wang, 2017a

## Slide 14
Related work – Wang 2017a
Source: Wang, 2017a

## Slide 15: 5929 Base Stations (BSs), 1.5 million users In-tower and inter-tower traffic Temporal correlations between physically distant towers Graph Neural Network (GNN) architecture
Related work – Wang 2017b
Source: Wang, 2017b
Notes: Correlações causadas por modais de transporte cada vez mais eficientes

## Slide 16
Related work – Wang 2017b
Source: Wang, 2017b
Notes: Correlações causadas por modais de transporte cada vez mais eficientes

## Slide 17
Related work – Summary
Ref. | Method | Dataset availability | Source code available
(Wang et al., 2017a) | Autoencoders | X | X
(Wang et al., 2017b) | Graph Neural Networks | X | X
(Sciancalepore et al., 2017) | Holt Winters | No information | X
(ALAWE et al., 2018) | Deep Learning | X | X
(YANG et al., 2021) | ARIMA and Neural Network | ✓ | X
Notes: Cada um considera métodos de modelagem diferentes
De qualquer forma, o custo computacional tende a ser maior com técnicas mais complexas

## Slide 18
Related work – Summary
Ref. | LSTM | Time series | Grid arrange | Neighborhood concept | Spatial modelling | Residual/aperiodic events | Network traffic consumption characterization
Wang et al., 2015 |  |  |  |  |  |  | ✓
Wang et al., 2017a | ✓ |  | ✓ | ✓ | ✓ |  | 
Wang et al., 2017b |  | ✓ |  | ✓ | ✓ | ✓ | 
YANG et al., 2021 |  | ✓ |  |  |  |  | 
Gotzner; Rathgeber, 1998 |  |  |  |  |  |  | ✓
BOUTABA et al., 2018 |  |  |  |  |  |  | ✓
Notes: Cada um considera métodos de modelagem diferentes
De qualquer forma, o custo computacional tende a ser maior com técnicas mais complexas

## Slide 19: Contents
Introduction
Related Work
Preliminaries on data collection for MTP-NT
  Preliminaries
  The predictive model in the 5G infrastructure
  Data Flow
  Dataset used in this work
  Mathematical formalization
Framework structure and fundamentation
Experimental results
Final considerations and future work

## Slide 20
Preliminaries on data Collection for MTP-NT - Preliminaries
Lipsum

## Slide 21: Thanks!
Patrick Luiz de Araújo
patrick@ufu.br
Prof. Dr. Rafael Pasquini
rafael.pasquini@ufu.br
Prof. Dr. Murillo Guimarães Carneiro
mgcarneiro@ufu.br
A Mobile Traffic Predictor Enhanced by Neighboring Transportation Data (MTP-NT)