## Slide 1: A Mobile Traffic Predictor Enhanced by Neighboring Transportation Data (MTP-NT)
Patrick Luiz de Araújo
Programa de Pós-Graduação em Ciência da Computação
Defesa de dissertação de mestrado em 21/11/2023
Notes: 00:24

## Slide 2: Contents
Introduction
Related Work
Theoretical fundamentation
Preliminaries on data collection for MTP-NT
MTP-NT: Framework structure and fundamentation
Experimental results
Final considerations and future work
Notes: 00:48

## Slide 3: Data per month, per smartphone in 2028
19 GB/month
5G subscribers in 2028
5 billion
Data per quarter in 2028
100 exabytes
Introduction
Fonte: Ericsson Mobility Report, November 2022
Notes: 01:12

## Slide 4
To
Allocate the maximum amount of users
Introduction
New 5G networks will count on
Core Network (CN) based on Virtual Network Functions (VNF) over a Network Function Virtualization (NFV)2 topology
Cloud and edge computing3
Use Machine Learning (ML) and other predictive tools
Optimize network operability
Reach 5G QoS/QoE metrics1
1ms latency
low energy consumption
High coverage
[1] AGIWAL, M.; ROY, A.; SAXENA, N. Next generation 5g wireless networks: A comprehensive survey. IEEE Communications Surveys Tutorials, v. 18, n. 3, p. 1617–1655, 2016.
[2] Sun, Y. et al. Application of machine learning in wireless networks: Key techniques and open issues. IEEE Communications Surveys Tutorials, v. 21, n. 4, p. 3072–3108, 2019.
[3] ALAWE, I. et al. Improving traffic forecasting for 5g core network scalability: A machine learning approach. IEEE Network, v. 32, n. 6, p. 42–49, 2018.
Intelligent caching in network edge
Cloud computing optimization
Notes: [01:36]
NFV: topologia usando cloud e/ou edge
Estruturas com a capacidade que necessitam, economizando recursos
Vai passar a ter gerenciamento de rede unificado

## Slide 5
AI models advantages
Introduction
Limitants
Enough data?
Pertinent information?
Response time
Return Over Investiment – ROI
Rely on historical data123
Can be less complex than conventional approaches4
Robust patterns and best overall performance5
[1] Wang, X. et al. Spatio-temporal analysis and prediction of cellular traffic in metropolis. In: 2017 IEEE 25th International Conference on Network Protocols (ICNP). [S.l.: s.n.], 2017. p. 1–10
[2] Wang, J. et al. Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. In: IEEE INFOCOM 2017 - IEEE Conference on Computer Communications. [S.l.: s.n.], 2017. p. 1–9.
[3] CHEN, X. et al. Analyzing and modeling spatio-temporal dependence of cellular traffic at city scale. In: 2015 IEEE International Conference on Communications (ICC). [S.l.: s.n.], 2015. p. 3585–3591.
[4] SUN, H. et al. Learning to optimize: Training deep neural networks for wireless resource management. In: 2017 IEEE 18th International Workshop on Signal Processing Advances in Wireless Communications (SPAWC). [S.l.: s.n.], 2017. p. 1–6.
[5] Sun, Y. et al. Application of machine learning in wireless networks: Key techniques and open issues. IEEE Communications Surveys Tutorials, v. 21, n. 4, p. 3072–3108, 2019.
Notes: [02:00]
Modelos de IA
Dependem de dados históricos
Menos complexos: implementação de um alocador de potência menos complexo que o Weighted Minimum Mean-Square Error (WMMSE)

## Slide 6: tl;dr
Enough Data
Innovation
Compatible responsiveness
Performance
Notes: [02:24]
Estes são os desafios a atentar-se em uma implementação de ML em 5G

## Slide 7: Mobile Traffic Predictor Enhanced by Neighboring Transportation Data MTP-NT
City of Milan Dataset1
Network usage
Geolocalized tweets
Weather
Electricity
News
[1] Barlacchi, G. et al. A multi-source dataset of urban life in the city of milan and the province of trentino. Sci Data 2, 2015.
Notes: [02:48]
Dados
GDPR: politica de dados robusta
Dados de 1/nov/2013 até 31/dez/2013

## Slide 8: Mobile Traffic Predictor Enhanced by Neighboring Transportation Data MTP-NT
City of Milan Dataset1
Scalable public transport and neighboring data
Open source
Network usage
Geolocalized tweets
Weather
Electricity
News
[1] Barlacchi, G. et al. A multi-source dataset of urban life in the city of milan and the province of trentino. Sci Data 2, 2015.
Notes: [03:12]
Inovação
Uso pioneiro de dados de transporte público
Dados e modelagem abertas na licença CC 4.0
Uso de feature selection para diminuir o custo computacional de treinamento e inferência do modelo

## Slide 9: Mobile Traffic Predictor Enhanced by Neighboring Transportation Data MTP-NT
City of Milan Dataset1
Scalable public transport and neighboring data
Open source
Lightweight, adaptable and highly performant
Network usage
Geolocalized tweets
Weather
Electricity
News
[1] Barlacchi, G. et al. A multi-source dataset of urban life in the city of milan and the province of trentino. Sci Data 2, 2015.
Notes: [03:36]
Leve
Escalável através do volume de dados ingeridos
Vários volumes validados

## Slide 10: Mobile Traffic Predictor Enhanced by Neighboring Transportation Data MTP-NT
City of Milan Dataset1
Scalable public transport and neighboring data
Open source
Lightweight, adaptable and highly performant
State-of-art performance
Network usage
Geolocalized tweets
Weather
Electricity
News
[1] Barlacchi, G. et al. A multi-source dataset of urban life in the city of milan and the province of trentino. Sci Data 2, 2015.
Notes: [04:00]
Performático
Performance
Validação por diferentes meios
Diferentes regiões da cidade e grupos de testes
Manipulação da base para avaliar outros cenários

## Slide 11: Contents
Introduction
Related Work
  Introduction
  Network traffic characterization
  Network traffic prediction
Theoretical fundamentation
Preliminaries on data collection for MTP-NT
MTP-NT: Framework structure and fundamentation
Experimental results
Final considerations and future work
Notes: [04:24]

## Slide 12: Metrics and mathematical characteristics of network usage
Related work
Characterization
Prediction
Mathematical models to predict network traffic

## Slide 13: Regions of the city grouped based on network usage patterns1 Composition of trimodal distributions to describe the network traffic2 Sand temporal distribution of the network traffic results into extremely insufficient utilization of network resources2 Traffic was concentrated in some regions (city center) and peak hours3
Network Traffic Characterization
[1] Xu, F. et al. Understanding mobile traffic patterns of large scale cellular towers in urban environment. IEEE/ACM Transactions on Networking, v. 25, n. 2, p. 1147–1161, 2017.
[2] WANG, H. et al. Characterizing the spatio-temporal inhomogeneity of mobile traffic in large-scale cellular data networks. In: Proceedings of the 7th International Workshop on Hot Topics in Planet-Scale MObile Computing and
Online Social NeTworking. New York, NY, USA: Association for Computing
Machinery, 2015. (HOTPOST ’15), p. 19–24. ISBN 9781450335171. Disponível em: <https://doi.org/10.1145/2757513.2757518>.
[3] Gotzner, U.; Rathgeber, R. Spatial traffic distribution in cellular networks. In: VTC
’98. 48th IEEE Vehicular Technology Conference. Pathway to Global Wireless
Revolution (Cat. No.98CH36151). [S.l.: s.n.], 1998. v. 3, p. 1994–1998 vol.3.

## Slide 14: Grouping of regions based on network usage patterns
Characterization – Xu
Residential
Transport
Office
Entertainment
Comprehensive areas
Human labelling of some regions to generalization
Characteristics of traffic: temporal and frequency
Notes: [05:36]

## Slide 15: Weekday-Weekend Traffic Amount Ratio: ratio of weekdays and weekend traffic Peak-Valley Features: ratio of maximum and minimum traffic registered as seen in the figure ahead Time of Traffic Peak and Valley: time of the day of maximum and minimum network usage Discrete Fourier Transform (DFT)
Characterization – Xu
Notes: O artigo apresenta algumas das features usadas
Weekday-Weekend Traffic Amount Ratio: quão do tráfego está concentrado em dias úteis ou não
Peak-Valley Featres: discrepância do tráfego em momentos de pico e vale. Em regiões de transporte apresentou 133.33

## Slide 16
Characterization – Xu
Source: Xu, F. et al. Understanding mobile traffic patterns of large scale cellular towers in urban environment. IEEE/ACM Transactions on Networking, v. 25, n. 2, p. 1147–1161, 2017.
Notes: Caracterização de uma região de transporte

## Slide 17
Characterization – Xu
Source: Xu, F. et al. Understanding mobile traffic patterns of large scale cellular towers in urban environment. IEEE/ACM Transactions on Networking, v. 25, n. 2, p. 1147–1161, 2017.

## Slide 18: 380,000 Base Stations (BSs) in Shanghai August 1 – August 31, 2014 10 minute samples of each Base Station (BS) 1.96 billion entires; 28PB (92TB per day, 7GB per BS on average)
Characterization – Wang 2015
Source: WANG, H. et al. Characterizing the spatio-temporal inhomogeneity of mobile traffic in large-scale cellular data networks. In: Proceedings of the 7th International Workshop on Hot Topics in Planet-Scale MObile Computing and Online Social NeTworking. New York, NY, USA: Association for Computing Machinery, 2015. (HOTPOST ’15), p. 19–24. ISBN 9781450335171. Disponível em: <https://doi.org/10.1145/2757513.2757518>.
Notes: [07:12]
As amostras tiveram a mesma frequência da base usada no trabalho

## Slide 19: Findings Trimodal distribution
Characterization – Wang 2015
Compound-expontential
Power-law distribution
Exponential distribution
R-square of 99%

## Slide 20: Findings Spatial and temporal distribution of network traffic highly concentrated
Characterization – Wang 2015
Source: WANG, H. et al. Characterizing the spatio-temporal inhomogeneity of mobile traffic in large-scale cellular data networks. In: Proceedings of the 7th International Workshop on Hot Topics in Planet-Scale MObile Computing and Online Social NeTworking. New York, NY, USA: Association for Computing Machinery, 2015. (HOTPOST ’15), p. 19–24. ISBN 9781450335171. Disponível em: <https://doi.org/10.1145/2757513.2757518>.
Notes: A falta de homogeneidade causa um uso insuficiente da infraestrutura de rede

## Slide 21: Findings Irregular usage depending on the urban ecology
Characterization – Wang 2015
Source: WANG, H. et al. Characterizing the spatio-temporal inhomogeneity of mobile traffic in large-scale cellular data networks. In: Proceedings of the 7th International Workshop on Hot Topics in Planet-Scale MObile Computing and Online Social NeTworking. New York, NY, USA: Association for Computing Machinery, 2015. (HOTPOST ’15), p. 19–24. ISBN 9781450335171. Disponível em: <https://doi.org/10.1145/2757513.2757518>.
Notes: Reforçando a ideia da ecologia urbana

## Slide 22: Network traffic in Berlin May 1996 – August 1997 Findings
Characterization – Gotzner
Source: Gotzner, U.; Rathgeber, R. Spatial traffic distribution in cellular networks. In: VTC’98. 48th IEEE Vehicular Technology Conference. Pathway to Global Wireless Revolution (Cat. No.98CH36151). [S.l.: s.n.], 1998. v. 3, p. 1994–1998 vol.3.
Traffic concentrated in city centre
Congestions in peak hours
Network resources not fully used in other points
The infrastructure reaches the maximum capacity before all processing power request
Notes: [08:48]
A infraestrutura chega ao seu limite de atendimento antes de ser integralmente ocupada

## Slide 23
[1] BOUTABA, R. et al. A comprehensive survey on machine learning for networking: evolution, applications and research opportunities. Journal of Internet Services and Applications, Springer, v. 9, n. 1, p. 1–99, 2018.
[2] CYBENKO, G. Approximation by superpositions of a sigmoidal function. Mathematics of control, signals and systems, Springer, v. 2, n. 4, p. 303–314, 1989.[3] Funahashi, 1989
[4] HORNIK, K. Approximation capabilities of multilayer feedforward networks. Neural networks, Elsevier, v. 4, n. 2, p. 251–257, 1991.[5] Wang, 2017a
[5] FUNAHASHI, K.-I. On the approximate realization of continuous mappings by neural networks. Neural networks, Elsevier, v. 2, n. 3, p. 183–192, 1989.
[6] Wang, X. et al. Spatio-temporal analysis and prediction of cellular traffic in metropolis. In: 2017 IEEE 25th International Conference on Network Protocols (ICNP). [S.l.: s.n.], 2017. p. 1–10.
[7] YANG, H. et al. A network traffic forecasting method based on sa optimized arima–bp neural network. Computer Networks, v. 193, p. 108102, 2021. ISSN 1389-1286. Disponível em: <https://www.sciencedirect.com/science/article/pii/ S1389128621001821>.
Network Traffic Prediction
Pure Time Series Function (TSF) and Non-TSF problem1
Multi Layer Perceptrion (MLP) to traffic perdiction2
Single Layer Perceptron (SLP) to traffic perdiction3
MLP to network traffic forecasting4
Recurrent Neural Network and usage of global + local autoencoders5
In-tower and inter-tower traffic analysis through a Graph Neural Network (GNN)6
AutoRegressive Moving Average (ARIMA) and Neural Network model training with Simulated Annealing (SA)7
2021
2017
1991
1989

## Slide 24: 2844 Base Stations (BSs) in Suzhou 500m2x 500m2 Uses the neighborhood concept LSTM Cells paired with Global and Local Autoencoders
Prediction – Wang 2017a
Source: Wang, J. et al. Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. In: IEEE INFOCOM 2017 - IEEE Conference on Computer Communications. [S.l.: s.n.], 2017. p .1–9.
Notes: [09:36]

## Slide 25
Prediction – Wang 2017a
Source: Wang, J. et al. Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. In: IEEE INFOCOM 2017 - IEEE Conference on Computer Communications. [S.l.: s.n.], 2017. p. 1–9.
Notes: Auto correlação do downlink e do uplink usando a Auto Correlation Function (ACF)
Picos de autocorrelação em múltiplos de 24h

## Slide 26
Prediction – Wang 2017a
Source: Wang, J. et al. Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. In: IEEE INFOCOM 2017 - IEEE Conference on Computer Communications. [S.l.: s.n.], 2017. p. 1–9.
Notes: Correlação espacial
Cada torre estava subsequentemente a leste da anterior
Parte superior: uplink; Parte inferior: downlink

## Slide 27
Prediction – Wang 2017a
Source: Wang, J. et al. Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. In: IEEE INFOCOM 2017 - IEEE Conference on Computer Communications. [S.l.: s.n.], 2017. p. 1–9.
Notes: O modelo possui um arranjo de autoencoders locais bem como um autoencoder global
O autoencoder global é treinado com base nos autoencoders locais
Os arranjos são somados (append) e inseridos em redes temporais (LSTMs)

## Slide 28
Prediction – Wang 2017a
Source: Wang, J. et al. Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. In: IEEE INFOCOM 2017 - IEEE Conference on Computer Communications. [S.l.: s.n.], 2017. p. 1–9.
Notes: Uma comparação da performance em comparação ao número de unidades do LSAE foi feita
Uma comparação paralela foi feita no trabalho desenvolvido

## Slide 29: 5929 Base Stations (BSs), 1.5 million users In-tower and inter-tower traffic
Related work – Wang 2017b
Source: Wang, X. et al. Spatio-temporal analysis and prediction of cellular traffic in metropolis. In: 2017 IEEE 25th International Conference on Network Protocols (ICNP). [S.l.: s.n.], 2017. p. 1–10.
Notes: [11:36]
Correlações causadas por modais de transporte cada vez mais eficientes

## Slide 30
Related work – Wang 2017b
Source: Wang, X. et al. Spatio-temporal analysis and prediction of cellular traffic in metropolis. In: 2017 IEEE 25th International Conference on Network Protocols (ICNP). [S.l.: s.n.], 2017. p. 1–10.
Notes: Conforme visto, regiões de transporte apresentam tráfego com alta mobilidade

## Slide 31: Temporal correlations between physically distant towers Graph Neural Network (GNN) architecture
Related work – Wang 2017b
Source: Wang, X. et al. Spatio-temporal analysis and prediction of cellular traffic in metropolis. In: 2017 IEEE 25th International Conference on Network Protocols (ICNP). [S.l.: s.n.], 2017. p. 1–10.
Notes: Correlações causadas por modais de transporte cada vez mais eficientes

## Slide 32
Related work – Wang 2017b
Source: Wang, X. et al. Spatio-temporal analysis and prediction of cellular traffic in metropolis. In: 2017 IEEE 25th International Conference on Network Protocols (ICNP). [S.l.: s.n.], 2017. p. 1–10.
Notes: Correlações causadas por modais de transporte cada vez mais eficientes

## Slide 33
Related work – Summary
Ref. | Method | Dataset availability | Source code available
(Wang et al., 2017a) | Autoencoders | X | X
(Wang et al., 2017b) | Graph Neural Networks | X | X
(Sciancalepore et al., 2017) | Holt Winters | No information | X
(ALAWE et al., 2018) | Deep Learning | X | X
(YANG et al., 2021) | ARIMA and Neural Network | ✓ | X
Notes: [13:12]
Fazendo um copilado dos principais métodos e disponibilidade de dados e código fonte
Cada um considera métodos de modelagem diferentes

## Slide 34
Related work – Summary
Ref. | LSTM | Time series | Grid arrange | Neighborhood concept | Spatial modelling | Residual/aperiodic events | Network traffic consumption characterization
Wang et al., 2015 |  |  |  |  |  |  | ✓
Wang et al., 2017a | ✓ |  | ✓ | ✓ | ✓ |  | 
Wang et al., 2017b |  | ✓ |  | ✓ | ✓ | ✓ | 
YANG et al., 2021 |  | ✓ |  |  |  |  | 
Gotzner; Rathgeber, 1998 |  |  |  |  |  |  | ✓
BOUTABA et al., 2018 |  |  |  |  |  |  | ✓
Notes: Agora expandindo as técnicas utilizadas
E amarrando com as principais técnicas do nosso trabalho

## Slide 35: Contents
Introduction
Related Work
Theoretical fundamentation
  Introduction
  Neural networks development and training
  LSTM
  Feature selection
Preliminaries on data collection for MTP-NT
Framework structure and fundamentation
Experimental results
Final considerations and future work
Notes: [14:00]

## Slide 36
Theoretical fundamentation – Neural networks development and training
Source: the author
Common activation functions:
Sigmoid: output between 0 and 1;
Hyperbolic tangent: output -1 and 1;
Rectified Linear Unit (ReLU)
Notes: [14:24]
Treinar uma rede neural = adaptar os pesos para minimizar o erro e=|y – y^|
Backpropagation: uma forma de treinar a rede neural; amarra o erro a variação dos pesos

## Slide 37
Theoretical fundamentation – LSTM
Source: the author
Notes: [14:48]

## Slide 38: Mainly used to dimensionality reduction Pearson correlation coefficient
Theoretical fundamentation – Feature selection
Between -1 and 1
Strength of the relationship between two variables
f-value Distance based algorithm
All transport regions inside 20 Moore distance*
*Later explained
Notes: [15:12]
A redução da dimensionalidade visa minimizar a perda de performance retirando as características menos relacionadas ao alvo
Menos custos computacionais
Menos ruído
Feature seletion
Pearson: o quão duas variáveis são relacionadas
F-test: quão da variação de uma variável dependente pode ser explicada pela variação de uma outra variável
Moore: todos os hubs de transporte em uma distância de moore máxima de 20 unidades

## Slide 39: Contents
Introduction
Related Work
Theoretical fundamentation
Preliminaries on data collection for MTP-NT
  Preliminaries
  The predictive model in the 5G infrastructure
  Data Flow
  Dataset used in this work
  Mathematical formalization of dataset preprocessing
Framework structure and fundamentation
Experimental results
Final considerations and future work
Notes: [15:36]

## Slide 40
Preliminaries on data Collection for MTP-NT – The predictive model in the 5G Infrastructure
Source: the author
Notes: [16:00]
Serviços baseados em hardware proprietário, tais como:
IDS
Proxy
Criptografia
Monitoramento de rede
Desvantagens
Ciclo de aquisição -> treinamento -> deploy custosos e rápidos
Sistema estático
Não escalável
Dependente do fornecedor
Padrões fechados

## Slide 41: Hardware middleboxes become software functions Rely on dedicated hardware and/or cloud
Preliminaries on data Collection for MTP-NT – The predictive model in the 5G Infrastructure
Network Function Virtualization (NFV)
Notes: Desvantagens
Ciclo de aquisição -> treinamento -> deploy custosos e rápidos
Sistema estático
Não escalável
Dependente do fornecedor
Padrões fechados
NFV
Hardware middleboxes -> VNF

## Slide 42
Preliminaries on data Collection for MTP-NT – The predictive model in the 5G Infrastructure
Source: the author
Notes: Nessa nova infraestrutura, um novo recurso passa a ser valioso: os recursos computacionais
Orquestrador
Encontra o melhor arranjo com base em métricas
Para ajudar o escalonador:
Network Traffic Monitoring and Analysis (NTMA)
VNF
Previsão de tráfego de rede

## Slide 43: Main advantages according to European Telecommunications Standards (ETSI)1
[1] ETSI, N. Network Function Virtualisation Use Cases. [S.l.]: European Telecommunications Standards Institute Sophia-Antipolis, France, 2013.
[2] RANKOTHGE, W. et al. Towards making network function virtualization a cloud computing service. In: IEEE. 2015 IFIP/IEEE International Symposium on Integrated Network Management (IM). [S.l.], 2015. p. 89–97.
[3] BASTA, A. et al. Applying nfv and sdn to lte mobile core gateways, the functions placement problem. In: Proceedings of the 4th workshop on All things cellular: operations, applications, & challenges. [S.l.: s.n.], 2014. p. 33–38.
[4] BRONSTEIN, Z.; SHRAGA, E. Nfv virtualisation of the home environment. In: IEEE.
2014 IEEE 11th Consumer Communications and Networking Conference (CCNC). [S.l.], 2014. p. 899–904.
[5] MANGILI, M.; MARTIGNON, F.; CAPONE, A. Stochastic planning for content delivery: Unveiling the benefits of network functions virtualization. In: IEEE. 2014 IEEE 22nd International Conference on Network Protocols. [S.l.], 2014. p. 344–349.
[6] KIM, T.; LEE, B. Scalable cdn service poc over distributed cloud management platform. In: IEEE. 2014 International Conference on Information and Communication Technology Convergence (ICTC). [S.l.], 2014. p. 832–833.
NFV as a service2
Virtualization of Core Network (CN) and Base Stations (BSs)3
Virtualization of home environment4
Virtualization of CDNs5,6
Preliminaries on data Collection for MTP-NT – The predictive model in the 5G Infrastructure
Notes: Alguns pontos de atenção
- Latêcia geral de uma cadeia de middleboxes

## Slide 44: Network Traffic Monitoring and Analysis Also a NFV Problems
Preliminaries on data Collection for MTP-NT – The predictive model in the 5G Infrastructure
Orchestrator
NTMA
Volume
Velocity
Network usage
Problems
Volume
Velocity
Notes: Nessa nova infraestrutura, um novo recurso passa a ser valioso: os recursos computacionais
Orquestrador
Encontra o melhor arranjo com base em métricas
Network Traffic Monitoring and Analysis (NTMA)
VNF
Previsão de tráfego de rede

## Slide 45: How does it flow? How to store? Is there a open standard?
Preliminaries on data Collection for MTP-NT – The predictive model in the 5G Infrastructure
Orchestrator
NTMA
Network usage
Notes: Nessa nova infraestrutura, um novo recurso passa a ser valioso: os recursos computacionais
Orquestrador
Encontra o melhor arranjo com base em métricas
Network Traffic Monitoring and Analysis (NTMA)
VNF
Previsão de tráfego de rede

## Slide 46: Flow collectors/Network exporters and collectors Radio Access Network (RAN) layer Network Data Analytics Function (NWDAF)1
Preliminaries on data Collection for MTP-NT – Data flow
[1] 3GPP. Architecture enhancements for 5G System (5GS) to support network data analytics services. [S.l.], 2022. Version 17.5.0. Disponível em: <<https://portal.3gpp. org/desktopmodules/Specifications/SpecificationDetails.aspx?specificationId=3579>>.
Notes: [18:24]
NWDAF é uma interface padrão do 5G
Pode se comunicar com a camada Policy Control Function (PCF)
PCF: camada de gestão de políticas de fatiamento

## Slide 47: NoSQL12 Less performance penalties with large datasets Popular open source solutions
Preliminaries on data Collection for MTP-NT – Data flow
[1] HAN, J. et al. Survey on nosql database. In: IEEE. 2011 6th international conference on pervasive computing and applications. [S.l.], 2011. p. 363–366.
[2] D’ALCONZO, A. et al. A survey on big data for network traffic monitoring and analysis. IEEE Transactions on Network and Service Management, IEEE, v. 16, n. 3, p. 800–813, 2019.
Notes: Armazenado para análises futuras

## Slide 48: The data is pulled by the MTP-NT, which can be seen as a NTMA
Preliminaries on data Collection for MTP-NT – Data flow

## Slide 49
Preliminaries on data Collection for MTP-NT – Data flow
Notes: Bases para registro das predições
Nnwdaf_AnalyticsSubscription service
- Serviço Publisher-subscriber
- Uso interno no core 5G

## Slide 50
Preliminaries on data Collection for MTP-NT – Data flow
Source: the author
Notes: Alguns pontos de atenção
- Latêcia geral de uma cadeia de middleboxes

## Slide 51: Database to Milan and Trento from November 1st to December 31st of 20131
[1] Barlacchi, G. et al. A multi-source dataset of urban life in the city of milan and the province of trentino. Sci Data 2, 2015.
Grid (Telecom Italia)
Social Pulse (Spazio Dati, DEIB)
Telecommunications (Telecom Italia)
Precipitations (Metereotrentino, ARPA)
Weather (ARPA)
Electricity (SET Distribuizione SPA)
News (Citynews)
Preliminaries on data Collection for MTP-NT – Dataset used in this work
Notes: [20:24]
Nem todas as bases de dados foram exploradas
Escolheu-se a cidade de Milão

## Slide 52: Telecommunications dataset from Milan
10,000 zonal regions in a 100x100 regular grid
Each regions is a square of 0.06km2
One log at every 10 minutes in every region
Call Detail Records (CDRs)
  Every time an user initiates or ends a network connection;
  For a given connection, an additional CDR is generated every 15 additional minutes of connection or if the user transfers more than 5MB over the internet;
  Other origins as SMS and calls, but this information is not used in this work.
Preliminaries on data Collection for MTP-NT – Dataset used in this work
Notes: Os grids são regulares apesar da cobertura das torres não ser
- Anonimização dos dados que será explorada mais adiante

## Slide 53: Anonymization of data
GDPR compliant
Protects the real infrastructure capabilities
Each parameter is multiplied by a anonymization constant
Preliminaries on data Collection for MTP-NT – Dataset used in this work
Notes: De acordo com a GDPR: não possibilita rastreamento de um único usuário
Também mantém reservado a capacidade real da infraestrutura da Telecom Italia

## Slide 54
Preliminaries on data Collection for MTP-NT – Dataset used in this work
Notes: De acordo com a GDPR: não possibilita rastreamento de um único usuário
Também mantém reservado a capacidade real da infraestrutura da Telecom Italia

## Slide 55
Preliminaries on data Collection for MTP-NT – Dataset used in this work
Source: Barlacchi
Notes: Gráfico superior
Cada região tem seu padrão de tráfego
Bocconi: universidade; redução do tráfego aos finais de semana
Duomo e Navigli: tráfego mais intenso, majoritariamente de regiões turísticas
Navigli: bairro turístico com grande tráfego no período noturno
Gráfico inferior
- Bosco fica quase imperceptível por ser menos movimentado

## Slide 56: Sudden changes in network usage can make predictions inaccurate1 Despite changes, patterns can be identified and models could be developed2 Traffic “hubs” can be a good source of information to traffic prediction3,4
[1 D’ALCONZO, A. et al . A survey on big data for network traffic monitoring and analysis. IEEE Transactions on Network and Service Management, v. 16, n. 3, p. 800–813, 2019.
[2] PIROZMAND, P. et al. Human mobility in opportunistic networks: Characteristics, models and prediction methods. Journal of Network and Computer Applications, Elsevier, v. 42, p. 45–58, 2014.
[3] WANG, H. et al. Characterizing the spatio-temporal inhomogeneity of mobile traffic in large-scale cellular data networks. In: Proceedings of the 7th International Workshop on Hot Topics in Planet-Scale MObile Computing and Online Social NeTworking. New York, NY, USA: Association for Computing Machinery, 2015. (HOTPOST ’15), p. 19–24. ISBN 9781450335171. Disponível em: <https://doi.org/10.1145/2757513.2757518>.
[4] Wang, X. et al. Spatio-temporal analysis and prediction of cellular traffic in metropolis. In: 2017 IEEE 25th International Conference on Network Protocols (ICNP). [S.l.: s.n.], 2017. p. 1–10.
Preliminaries on data Collection for MTP-NT – Dataset used in this work
Notes: Sudden changes:
Rede pode ter um comportamento irregular
Fundamentalmente, em redes móveis, estamos falando do comportamento humano
Traffic “hubs”:
Pessoas se deslocam em transporte público
Transporte cada vez mais eficiente
Cria correlações entre regiões fisicamente distantes

## Slide 57
Preliminaries on data Collection for MTP-NT – Dataset used in this work
Source: the author
Notes: Azul: metro
Verde: bonde
Vermelho: ônibus
Dados coletados com a API do Google Maps

## Slide 58: Contents
Introduction
Related Work
Theoretical fundamentation
Preliminaries on data collection for MTP-NT
Framework structure and fundamentation
  Mathematical formalization of MTP-NT operations
  MTP-NT’s framework architecture
Experimental results
Final considerations and future work
Notes: [23:36]

## Slide 59: 10,000 regions 1 CDR sample for each 10 minutes, from November 1st to December 31st of 2013. Total: 8928 traffic samples for each region
Framework structure and fundamentation – Mathematical formalization of MTP-NT operations
Region for between 0 and 99
Time period between to
Notes: [24:00]

## Slide 60: Moore neighborhood
For a region the group of neighbors within a degree of distance is the group
Framework structure and fundamentation – Mathematical formalization of MTP-NT operations

## Slide 61
Scales with the increment of moore neighborhoods
Framework structure and fundamentation – Mathematical formalization of MTP-NT operations

## Slide 62: : Set of transport hubs : Feature selection to choose the most pertinent transport hubs to the given region : Group of transport hubs selected to a given region
Framework structure and fundamentation – Mathematical formalization of MTP-NT operations

## Slide 63
Framework structure and fundamentation – Mathematical formalization of MTP-NT operations
Notes: Branch 1
Input data from the selected neighbords
Selected time series transport hubs

## Slide 64
Framework structure and fundamentation – Mathematical formalization of MTP-NT operations
Notes: Branch 2
Vizinhos selecionados com base na distância de Moore
Séries temporais dos hubs de transporte selecionados
Algumas técnicas de seleção de variáveis foram testadas
A melhor seleção foi o uso dos 20 hubs mais próximos

## Slide 65
Source: the author
Framework structure and fundamentation – Mathematical formalization of MTP-NT operations

## Slide 66: Branch 1
MTP-NT’s framework architecture
Decode the input and begin the compression 𝐼𝑛𝑝𝑢𝑡_𝑜𝑡ℎ𝑒𝑟; 𝐸𝑛𝑐𝑜𝑑𝑖𝑛𝑔_𝑜𝑡ℎ𝑒𝑟_1
Temporal relations 𝐿𝑆𝑇𝑀_𝑜𝑡ℎ𝑒𝑟_1; 𝐷𝑟𝑜𝑝𝑜𝑢𝑡_𝑜𝑡ℎ𝑒𝑟_1
Temporal relations 𝐿𝑆𝑇𝑀_𝑜𝑡ℎ𝑒𝑟_2; 𝐷𝑒𝑐𝑜𝑑𝑒𝑟_𝑜𝑡ℎ𝑒𝑟_1; 𝐷𝑟𝑜𝑝𝑜𝑢𝑡_𝑜𝑡ℎ𝑒𝑟_2
General purpose correlations and reduce overfitting 𝐷𝑒𝑛𝑠𝑒_𝑜𝑡ℎ𝑒𝑟_2; 𝐷𝑟𝑜𝑝𝑜𝑢𝑡_𝑜𝑡ℎ𝑒𝑟_3
Concatenation of Branches 𝐷𝑒𝑛𝑠𝑒_𝑜𝑡ℎ𝑒𝑟_3
Notes: [26:48]

## Slide 67: Branch 2
MTP-NT’s framework architecture
Input layer 𝐼𝑛𝑝𝑢𝑡_y
Temporal relations 𝐿𝑆𝑇𝑀1; 𝐷𝑟𝑜𝑝𝑜𝑢𝑡1 𝐿𝑆𝑇𝑀2;𝐷𝑟𝑜𝑝𝑜𝑢𝑡2
General purpose correlations and reduce overfitting 𝐷𝑒𝑛𝑠𝑒1 𝐷𝑟𝑜𝑝𝑜𝑢𝑡3; 𝐷𝑒𝑛𝑠𝑒2
Concatenation of Branches 𝐷𝑒𝑛𝑠𝑒2
Notes: Step 2
- 144 units (24 hours of information in 10-minute samples)
- Dropout: randonly deactivate a sample of LSTM cells (10%)
Step 3
- Addition of a dense as a improvement in tests

## Slide 68: Concatenate and output step
MTP-NT’s framework architecture
Notes: Concatenate
Output

## Slide 69
MTP-NT’s framework architecture
Source: the author

## Slide 70: Contents
Introduction
Related Work
Theoretical fundamentation
Preliminaries on data collection for MTP-NT
MTP-NT: Framework structure and fundamentation
Experimental results
  Experimental setup
  Results
  Execution time evaluation
  Performance Analysis
Final considerations and future work
Notes: [28:24]

## Slide 71: Moore regions: 1; 1~2; 1~3; … ; 1~5
Experimental results - Setup
Notes: [28:48]

## Slide 72: Moore regions: 1; 1~2; 1~3; … ; 1~5
Experimental results - Setup
Feature selection algorithms
F-test
Pearson correlation coeficient
Moore test
Notes: Feature seletion
F-test: quão da variação de uma variável dependente pode ser explicada pela variação de uma outra variável
Pearson: o quão duas variáveis são relacionadas
Moore: todos os hubs de transporte em uma distância de moore máxima de 20 unidades

## Slide 73: Moore regions: 1; 1~2; 1~3; … ; 1~5
Experimental results - Setup
Feature selection algorithms
F-test
Pearson correlation coeficient
Moore test
Tests
Distributed tests
Core tests
Event regions
Notes: Tests
Distributed: 64 regiões homogeneamente espaçadas; Visa ilustrar de forma homogênea a cidade
Core: regions turísticas e/ou públicas. Ex.: Navigli, Luigi Bocconi University
Event: San Ciro/Giuseppe Meazza Stadium

## Slide 74
Experimental results - Setup
Source: the author

## Slide 75: Moore regions: 1; 1~2; 1~3; … ; 1~5
Experimental results - Setup
Feature selection algorithms
F-test
Pearson correlation coeficient
Moore test
Tests
Distributed tests
Core tests
Event regions
Variations
With transport hubs
Without transport hubs

## Slide 76: Evaluation metric
Experimental results - Setup

## Slide 77: Descendent error
Experimental results - Results
Source: the author
Notes: [31:12]

## Slide 78: Better overall performance, specially in:
Experimental results - Results
Outliers
Lower Moore distance models
Source: the author

## Slide 79
Experimental results - Results
Source: the author

## Slide 80: Considerations of transport hubs
Experimental results - Results
Can be important to anticipate fast changing demand from non-seasonal events1
More important in central regions of the city
Region 607 (near Vigano)
Normal tests:
Transport hubs tests:
[1] Wang, J. et al. Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. In: IEEE INFOCOM 2017 - IEEE Conference on Computer Communications. [S.l.: s.n.], 2017. p. 1–9.
Source: the author
Notes: Região periférica
Tráfego de rede mais algo (provavelmente picos anormais) não são cobertos

## Slide 81: Considerations of transport hubs
Experimental results - Results
Can be important to anticipate fast changing demand from non-seasonal events1
More important in central regions of the city
Region 8169 (mall near Parco Nord Milano)
Normal tests:
Transport hubs tests:
Source: the author
[1] Wang, J. et al. Spatiotemporal modeling and prediction in cellular networks: A big data enabled deep learning approach. In: IEEE INFOCOM 2017 - IEEE Conference on Computer Communications. [S.l.: s.n.], 2017. p. 1–9.
Notes: Região central
Picos de demanda de tráfego estão sendo cobertos

## Slide 82
How can MTP-NT perform in a different scenario?
Experimental results - Results
Notes: Diferentes janelas de tempo podem ser úteis em diferentes cenários
Compilações condizentes com um ajuste menos frequente nas especificações da infra
Base de treinamento ficou 6x menor
Mesmo assim não houve uma perda considerável de performance
Treinamento baixou de 175s~200s para 40s

## Slide 83
Experimental results – Execution Time Evaluation
Growth of regions with the maximum Moore distance considered
Notes: [33:36]

## Slide 84
Experimental results – Execution Time Evaluation
Source: the author
Notes: Adição dos hubs de transporte não implicam diretamente em um tempo de treinamento maior

## Slide 85
Experimental results – Performance Analysis
Auto Regressive Integrated Moving Average - ARIMA
Autoregression: self correlation (p)
Integration: stationary time series (d)
Moving Average: relation between error of previous samples and the actual (q)
Notes: [34:24]
Fazendo uma comparação com outras técnicas: ARIMA

## Slide 86
Experimental results – Performance Analysis
Auto Regressive Integrated Moving Average – ARIMA
Best model: p=36;d=1;q=0

## Slide 87
Experimental results – Performance Analysis
Holt-Winters (HW) model: aditive trend
Prophet: daily and weenkly seazonality
LSTM model
Standard scaler
128-cell LSTM layer + Dropout (10%)
128-cell LSTM layer + Dropout (10%)
Dense layer

## Slide 88
Experimental results – Performance Analysis
Notes: Bons resultados de forma geral
Testes Core e Event com a mesma performance de forma geral
- Indica que eventos aperiódicos não são um problema para o modelo

## Slide 89
Experimental results – Performance Analysis
(Wang 2017b) 45% drop in error compared to LSTM
MTP-NT: 77%
(Wang 2017b) 62% drop in error compared to HW
MTP-NT: similar
Notes: ARIMA
Tende a fazer previsões em torno das médias passadas
Não indicado para cenários muito dinâmicos

## Slide 90
Experimental results – Performance Analysis
Notes: HW
Basicamente repetindo as amostras anteriores
Boas métricas, mas pouco uso prático

## Slide 91
Experimental results – Performance Analysis
Notes: Teste de evento
Evento aperiódico sendo previsto pelo modelo
NMAE
11% (c/ hubs)
11,59% (sem hubs de transporte)

## Slide 92: Contents
Introduction
Related Work
Preliminaries on data collection for MTP-NT
Framework structure and fundamentation
Experimental results
Final considerations and future work
Notes: [37:12]

## Slide 93: Scenario in 5G
Data driven technologies in mobile networks
Notes: [37:36]

## Slide 94: Scenario in 5G
Data driven technologies in mobile networks
Large urban centers
Dynamic scenarios
Patterns and irregular factors
Strict QoS/QoE metrics

## Slide 95: Scenario in 5G
Data driven technologies in mobile networks
Large urban centers
Cloud based and compatible with 3GPP architecture purposals
Dynamic scenarios
Patterns and irregular factors
Strict QoS/QoE metrics
Notes: Virtualização da infraestrutura
Coletores de dados

## Slide 96: Scenario in 5G
Data driven technologies in mobile networks
Large urban centers
Cloud based architecture; 3GPP architecture purposal
GDPR and other major privacy policies
Dynamic scenarios
Patterns and irregular factors
Strict QoS/QoE metrics

## Slide 97: MTP-NT
Public transport hubs
As a way to bring new information to the model
Improve the coverage of aperiodic events
Notes: [39:12]

## Slide 98: MTP-NT
Public transport hubs
Performance aligned with state of art research
As a way to bring new information to the model
Improve the coverage of aperiodic events

## Slide 99: MTP-NT
Public transport hubs
Performance aligned with state of art research
Performance and accuracy tradeoff
As a way to bring new information to the model
Improve the coverage of aperiodic events
The model is flexible and allows a configuration to best fit the accuracy-model size best scenario

## Slide 100: MTP-NT
Public transport hubs
Performance aligned with state of art research
Performance and accuracy tradeoff
Multiple tests to ensure the performance
As a way to bring new information to the model
Improve the coverage of aperiodic events
The model is flexible and allows a configuration to best fit the accuracy-model size best scenario
Distributed
Core
Event
1-hour compilling

## Slide 101: MTP-NT
Public transport hubs
Performance aligned with state of art research
Performance and accuracy tradeoff
Multiple tests to ensure the performance
As a way to bring new information to the model
Improve the coverage of aperiodic events
The model is flexible and allows a configuration to best fit the accuracy-model size best scenario
Distributed
Core
Event
1-hour compilling
Open-source

## Slide 102: Future work
Heavier models
GPUs and other advancements make cloud computing cheaper
MTP-NT compiles a single region at a time
A new multi-region architecture can be better
More neighborhoods
Multi-region model
Notes: [40:00]

## Slide 103: Thanks!
Patrick Luiz de Araújo
patrick@ufu.br
Prof. Dr. Rafael Pasquini
rafael.pasquini@ufu.br
Prof. Dr. Murillo Guimarães Carneiro
mgcarneiro@ufu.br
A Mobile Traffic Predictor Enhanced by Neighboring Transportation Data (MTP-NT)